Circuits PhET Lab
Introduction to Physics

Introduction: Wouldn’t it be great to see inside wires and electrical devices, to actually watch the electrons flow? This simulation allows us to do this. In this sim, you will build simple and compound circuits and measure their potential (voltage), current, and resistance.

Important Formulas:
V=IR
Series: Rtot = R1 + R2 + R3 + …..	Vtot = V1 + V2 + V3 + ….
Parallel: 1/Rtot = 1/R1 + 1/R2 + 1/R3 + …..	Itot = I1 + I2 + I3 ...

Procedure: PheT Sims Play  Electricity, Magnets, and Circuits  Circuit Construction Kit (AC+DC)
- To add elements to your circuits, simply drag an item into the work area.
- To remove an item or change it, right-click the item you wish to change.
- To uncouple two circuit elements, right click on the circular junction and choose “split junction.”
- To measure voltage and current, click on the boxes to the left.
- Remember, voltage is read in parallel (outside of the circuit), while current is read in series (in the circuit)

Part I: DC Circuits in Series
Build a simple circuit made of one battery and one light in a single loop.
Draw your circuit: Use proper symbols (not real life)
What is the voltage drop across the light?

Light: ________________ Volts

What is the current of the circuit?
Light: ________________ Amps

Use Ohm’s Law to find the resistance of the light	Light: ________________ Ohms

Set both of the voltmeter’s probes on the same side of a light. What is the voltage? _____ Why?

Reverse the battery. What happens to the flow of electrons?

Build a circuit made a battery and three lights in series.

        Draw your circuit: Use proper symbols.

What are the voltage drops in the circuit?
Light 1: ________________ Volts
Light 2: ________________ Volts
Light 3: ________________ Volts
Battery: ________________ Volts

What is the current in each part of the circuit?
Between Bat and Light 1: _____________ Amps	Use Ohm’s Law to find the resistance of the lights
Between Lights 1-2: __________________ Amps	Light 1: ________________ Ohms
Between Lights 2-3: __________________ Amps	Light 2: ________________ Ohms
Battery: ____________________________Amps	Light 3: ________________ Ohms

Are all the lights the same brightness? _______

Remove a light from the circuit and reclose the circuit. What happens to the brightness of the other lights?

For a series circuit, as lights (with resistance) are added, the voltage:

For a series circuit, as lights (with resistance) are added, the current:

Add additional batteries in series with the first battery.
What happens to the brightness? ____________the voltages? ____________the currents? ____________
Add a resistor to your series circuit.
What effect did the resistor have on the lights in the circuit?

Create a wire path in your circuit that bypasses all the lights. This is a short circuit.
What happens to the battery in short circuit? ____________________ The lights? ___________________
What happens to electrons that are not slowed by the resistance of lights?

Part II: DC Circuits in Parallel
Build a circuit made a battery pack and three lights in parallel with the battery

Draw your circuit: Use proper symbols.

What are the voltage drops in the circuit?
Light 1: ________________ Volts
Light 2: ________________ Volts
Light 3: ________________ Volts
Battery: ________________ Volts

What is the current in each part of the circuit?
Light 1’s path: __________________ Amps	Use Ohm’s Law to find the resistance of the lights
Light 2’s path: __________________ Amps	Light 1: ________________ Ohms
Light 3’s path: __________________ Amps	Light 2: ________________ Ohms
Battery: ________________________Amps	Light 3: ________________ Ohms

Are all the lights the same brightness? _______

Remove a light from its path. What happens to the brightness of the other lights?

For a parallel circuit, as lights (with resistance) are added, the voltage:

For a parallel circuit, as lights (with resistance) are added, the current

Add additional batteries in series with the first battery.
What happens to the brightness? ______________the voltages? ______________the currents?_____________

Add a resistor to one path in your parallel circuit.
What effect did the resistor have on the light in its path?

What effect did the resistor have on the lights in the other two paths?