# Hooke's Law Lab
Introduction to Physics

Introduction:
The purpose of this experiment is to find the spring constant, or the stiffness, of a spring. This is done by measuring the displacement (change in position: final position – initial position) and the force (a push or pull exerted on an object that causes a change in motion) of the spring, testing how far the spring would stretch with a certain weight past equilibrium.
Variables:
- Dependent Variables (variables that are measured):
o Spring’s displacement
o Force
- Independent Variables (Variables that are controlled):
o How much weight/mass was put on the spring
o Spring (should be kept constant through out the experiment)

Procedure
1. After putting together what will hold up your spring, connect the spring and leave it hanging vertically with no weights/masses put on. This is the spring’s equilibrium. Measure it.
2. Next, chose a weight and attach it to your spring.
3. Measure (once spring has stopped bouncing) the length of the spring with weight attached.
4. MAKE SURE: you are measuring from the same spots of spring each time! Also make sure that you convert cm to m and g to kg!
5. Using Hooke’s law (F = -k x) solve for k.
6. Repeat this at least 3 more times with different weights (ex: 200g, 300g, 400g, 500g, etc.), so that there is more evidence to support your conclusion.
7. Record your data and make a graph.

Safety Precautions:
Be sure to move anything that is easily broken, just in case the spring goes flying off or the weight falls off (this shouldn’t happen, but just in case it does, be prepared).

Data collection:

Mass	Equilibrium Length	Equilibrium Length + Length with mass	Displacement	Force	Spring Constant
200 g
300 g
400 g
500 g

Graph: