Name	Period

Newton’s 2nd Law Lab

Purpose
To investigate the effect of increases in mass and applied force on the acceleration of a system.

Required Equipment and Supplies
stopwatch	meterstick	masking tape	dynamics cart
string	hook mass set	pulley with table clamp	graph paper

Discussion
Both mass and force affect the acceleration of an object. In the first part of this lab, the mass will vary, but the applied force will remain constant. In this case it is possible to discover the relationship between mass and acceleration.

In the second part of this lab, the mass will remain constant while the applied force varies. The applied force is increased without changing the mass by removing mass from the cart and placing it on the hanging mass. In this case it is possible to discover the relationship between applied force and acceleration.

Pulleys are devices that change the direction of a force without changing the magnitude of force. The pulley in this lab will change the direction of the force from a downward pull on the mass into a sideways pull on the cart.

Procedure
Fasten a pulley over the edge of the table.

Measure the height from the pulley to the floor. Mark off a distance on the top of the table slightly shorter than the distance from the pulley to the floor. Record this distance as the accelerating distance in Data & Observations.

Place a 1 kg mass on the dynamics cart. Tie one end of the string to the cart and thread it over the pulley attaching the free end to a 100 g mass as shown in the figure to the right. Stop the cart before it crashes in the pulley!

The mass of the cart is 200 g. Combine the mass of the cart, the mass in the cart, and the hanging mass to calculate the total mass of the system in kg and put this value in the correct column in the Changing Mass Data Table in Data & Observations.

Practice accelerating the cart a few times to ensure proper alignment. Keep 100 g falling mass the same at all times during the experiment, which keeps the applied force constant.

Use a stopwatch to time the cart over the distance marked off on the table. Do not allow the falling mass to touch the floor or the cart to crash into the pulley during this distance. Perform three time trials, recording the times in the appropriate place in the Changing Mass Data Table in Data & Observations.

Repeat step 6 four more times, each time removing mass (100 g or 200 g) and setting it aside. Record the mass of the system (200 g cart, mass in cart, and 100 g hanging mass) in the Changing Mass Data Table making sure the total mass of the system is recorded in kilograms. The final trial will be the cart with no mass on it. Record all the times in the appropriate place in the Changing Mass Data Table in Data & Observations.

Reset the masses so that there is 1 kg in the cart and 100 g of hanging mass. In this section of the lab the amount of hanging mass will be varied to vary the applied force, but the total mass of the system will remain the same. Record the total amount of hanging mass in the appropriate section of the Changing Force Data Table in Data & Observations.

Use a stopwatch to time the cart over the distance marked off on the table. Do not allow the falling mass to touch the floor or the cart to crash into the pulley during this distance. Perform three time trials, recording the times in the appropriate place in the Changing Force Data Table in Data & Observations.

Repeat step 6 four more times, each time removing mass (50 g or 100 g) from the cart and adding it the hanging mass. Record the total hanging mass in the Changing Force Data Table making sure the mass is recorded in kilograms. Record all the times in the appropriate place in the Changing Force Data Table in Data & Observations.

Clean up all lab supplies and equipment.

Calculate the average time for all mass and put this time in the appropriate place in each data table in Data & Observations.

Using the average time, calculate the acceleration of the system for all masses. Use the following equation to calculate the acceleration, with the distance or displacement equal to the acceleration distance measure in step 2 and an initial velocity of 0 m/s: . Record the acceleration in the appropriate place in the Changing Mass Data Table and in the Changing Force Data Table.

Data & Observations

Acceleration distance (m) ____________________

Changing Mass Data Table
Total mass of system (kg)	time (s) to cover same distance			Average / time (s)	Acceleration (m/s2)
	Trial 1	Trial 2	Trial 3

Changing Force Data Table
Total falling mass (kg)	time (s) to cover same distance			Average / time (s)	Acceleration (m/s2)
	Trial 1	Trial 2	Trial 3

Analysis
1. Create a graph of acceleration vs. mass using the data from the Changing Mass Data Table. Mass should be on the x-axis with acceleration on the y-axis. Make sure to have all the requirements for a standard graph.

2. Describe the graph of acceleration vs. mass, including the shape (straight line or curve) of the graph.

3. How does increasing the mass of an object affect its acceleration (for a constant applied force)?

4. Create a graph of acceleration vs. force using the data from the Changing Force Data Table. Force should be on the x-axis with acceleration on the y-axis. Make sure to have all the requirements for a standard graph.

5. Describe the graph of acceleration vs. force, including the shape (straight line or curve) of the graph.

6. How does increasing the applied force on an object affect its acceleration (for a constant mass)?

7. Combine the results of the relationship between acceleration and mass and the relationship between acceleration and force to develop a relationship between force, mass, and acceleration.