Resistance
Introduction to Physics

1. Electric eels, found in South America, can provide a potential difference of 440 V that draws a
      current of 0.80 A through the eel’s prey. Calculate the resistance of the circuit (the eel and prey).

2.	It is claimed that a certain camcorder battery can provide a potential difference of 9.60 V and a current of 1.50 A. What is the resistance through which the battery must be discharged?

3.	A prototype electric car is powered by a 312 V battery pack. What is the resistance of the motor circuit when 2.8  105 C passes through the circuit in 1.00 h?

4.	In 1992, engineers built a 2.5 mm long electric motor that can be driven by a very low emf. What is the potential difference if it draws a 3.8 A current through a 0.64  resistor?

5.	A team from Texas A&M University has built an electric sports car with a maximum motor current of 2.4  103 A. Determine the potential difference that provides this current if the circuit resistance is 0.30 .

6.	Stanford University scientists have constructed the Orbiting Picosatellite Automated Launcher (OPAL). OPAL can launch disposable “picosatellites” the size of hockey pucks. Each picosatellite will be powered by a 3.0 V battery for about an hour. If the satellite’s circuitry were to have a resistance of 16 , what current would be drawn by the satellite?

7.	For years, California has been striving for all zero-emission vehicles on its roads. In 1995, a street bus with a range of 120 km was built. This bus is powered by batteries delivering 6.00  102 V. If the circuit resistance is 4.4 , what is the current in the bus’s circuit?