Thermal Expansion
Introduction to Physics

Linear Expansion
Here is the equation:

∆L=αLO∆T

∆L is the change in length, in meters
α is the coefficient of linear expansion in ºC-1 (1/ºC)
LO is the original length in meters
∆T is the change in temperature in degrees Celsius

Let’s take a 1 meter steel bar.
αiron = 1.2 x 10-6 /ºC

∆L = (1.2 x 10-6) (1 meter) (500ºC)
    = .0006 m

Let’s double the temperature.

∆L = (1.2 x 10-6) (1 meter) (1000ºC)
     = .0012 m

So we can see there is a direct relationship between the change in temperature and the change in length.
Therefore we can say ∆L=∆T.

Let’s see what happens to an aluminum pan when it goes in an oven at 260ºC from a room temperature of 20ºC.
αaluminum = 2.3 x 10-5 /ºC

∆L = (23 x 10-6) (0.3 meter) (240ºC)
     = .0001656 m

Volumetric Expansion

Here is the equation

∆V=βVO∆T

∆V is the change in volume in cubic meters
β is the coefficient of volume expansion in ºC-1 (1/ºC)
VO is the original volume in cubic meters
∆T is the change in temperature in degrees Celsius

Interestingly enough, β = 3α

Let’s take a car’s gas tank. Of it has a capacity of 60 L at 20ºC, and it is filled to the top,
what happens if the car is left in the sun and the gas reaches a temp of 45ºC?
βgas = 9.5 x 10-4ºC-1

∆V = (9.5 x 10-4ºC-1) (60 L) (25ºC)
     = 1.4 L

Thus the tank will overflow and you will have 1.4 L of gas on the ground.

Area Expansion

Here is the equation:

∆A=(2α)AO∆T

∆A is the change in area, in cubic meters
α is the coefficient of linear expansion in ºC-1 (1/ºC)
AO is the original area in cubic meters
∆T is the change in temperature in degrees Celsius

Let us say that you have a lovely silver platter that you were given as a gift. Not thinking, you place it in the oven and raise the temperature from room temperature (25 ºC) to 260 ºC. The platter is a conveniently a nice
rectangle .05m by .03 m.
 αsilver = 1.8 x 10-5 ºC-1

∆A =(2) (1.8 x 10-5 ºC-1) (.05m x .03m) (235 ºC)
      = 1.3 x 10-5 m2