Wave Speed 2
Introduction to Physics

c = f%lambda

1. Scientists at Lucent Bell Labs use high-resolution microscopes to make images of tiny organisms that provide a lot of information. By using 3.2 nm (3x10-9 m) x-rays on human tissue, images can be made showing micro- tubules in the nuclei of cells. What is the frequency of these x-rays?

c =

f =

λ =

2. Suppose you must decide whether a pre-Columbian mask is genuine before buying it for a museum. It looks genuine, but to ensure its authenticity, you shine X rays of wavelength 1.67 × 10–10 m on it to see if a certain element is present. What is the frequency of this radiation?

c =

f =

λ =

3. Suppose you use ultraviolet light of frequency 9.5 × 1014 Hz to determine whether a mineral is fluorescent. To what wavelength does this correspond?

c =

f =

λ =

4. Meteorologists use Doppler radar to watch the movement of storms. If a weather station uses electromagnetic waves with a frequency of 2.85 × 109 Hz, what is the length of the wave?

c =

f =

λ =

5. In order to see objects, the wavelength of the light must be smaller than the object. The Bohr radius of a hydrogen atom is 5.291770 × 10–11 m. What is the lowest frequency that can be used to locate a hydrogen atom?

c =

f =

λ =

6. Suppose the microwaves in your microwave oven have a frequency of 2.5 × 1010 Hz.
a. What is the wavelength of these microwaves?
b. The holes in the door of a microwave oven have a radius of 1.2 mm. Why don’t microwaves pass through these holes?

c =

f =

λ =