Name	Period

Work and Power Lab

Purpose
To determine the relationships between work, power, and time.

Required Equipment and Supplies
stopwatch	meter stick	computer graphing software	stairwell

Discussion
Power is the rate at which work is done (P=W/t). Work is the force times the distance the force is applied (W=Fd). The standard unit of work is the joule (J) and the standard unit of power is the watt (W). The traditional unit of power used in the United States is “horsepower,” which is equal to approximately 746 watts (1 hp = 746 W).

A 0.01 horsepower (7.46 watt) motor is often used to power small clocks. A 0.25 horsepower (186.5 watts) motor is used in refrigerators. A 0.5 horsepower (373 watt) motor is used in a food processor. A 2 horsepower (1,492 watt) engine is often used to power lawnmowers. A scooter has 10 horsepower (7,460 watt) motor. Henry Ford used a 20 horsepower (14,920 watt) engine to power the famous Model-T that was dominant in the automotive market in the early 1900s. Today, some 8-cylinder automobile engines deliver 250 horsepower (186,500 watts) or more. The world’s most powerful motors are used in heavy industries and deliver more than 100,000 horsepower (74,600,000 watts). How powerful are you? Are you a small clock motor or closer to a car motor?

Procedure
- On the Work and Power Data Table in the Data and Observations section fill in the name of your classmates.
- Add each person’s weight in newtons (1 lb = 4.45 N).
- Measure the height of the stairwell by whatever means provided to you. This is the distance that will be run by each student. Record this distance in the labeled area in the Data and Observations section. Be sure to include units.
- Each person will climb the stairs as swiftly as they can while still being safe (no blood on the stairs and injuries cause extra paperwork).
- You will be timed to the nearest hundredth of a second.
- Record all of the times in the correct space in the table.
- Calculate each person’s work and power.

Data and Observations

distance: ____________________
Work and Power Data Table
Student Name	Weight (N)	Work (J)	Running Time (s)	Running Power (W)

Analysis
1. Create a graph of power vs. work. Plot work on the x-axis and power on the y-axis. Make sure the graph includes the following: title, x-axis, y-axis, labels and units for each axis, appropriate and constant scale, and data points.

2. Create a graph of work vs. time. Plot time on the x-axis and work on the y-axis. Make sure the graph includes the following: title, x-axis, y-axis, labels and units for each axis, appropriate and constant scale, and data points.

3. Create a graph of power vs. time. Plot time on the x-axis and power on the y-axis. Make sure the graph includes the following: title, x-axis, y-axis, labels and units for each axis, appropriate and constant scale, and data points.

4. Look at your power vs. work graph. Is there a general trend to your data? Explain.

5. Look at your work vs. time graph. Is there a general trend to your data? Explain.

6. Look at your power vs. time graph. Is there a general trend to your data? Explain.

7. Does doing more work necessarily mean you have more power? Explain.

8. Does it appear that gender has an effect on a person’s power? Explain.

9. Does doing the most work mean you have the most power and doing the least work mean you have the least power? Explain.

10. Suppose the height of the stairs was reduced by half.
a. How would this affect the work required to climb the stairs? Explain.

b. How would this affect the power required to climb the stairs? Explain.

11. What is your power in horsepower (1 hp = 746 W)?

12. Compare yourself to the horsepower of the motors described in the discussion section.
a. What could you power: a clock, refrigerator, food processor, lawnmower, scooter, Model-T, 8-cylinder engine, or industrious engine? Explain.

b. How many of the object you could power in part (a)?

13. Two students of equal weight go up the stairs. Student A walks up the stairs and Student B runs up the stairs. Which student does more work and which student has more power? Explain.

14. During times of dire emergency, people have been known to lift tremendous weights, such as the rear of a car to free a mechanic on whom the car has fallen.
a. Is greater work necessary to perform such feats than when lifting the same car the same distance using a jack? Explain.

b. Is greater power necessary to perform such feat than when lifting the same car the same distance using a jack? Explain.